## Slide 1: Energy Efficiency Potential in Saudi Arabia Building Sector
Dr. Naif M. Alabbadi SEEC, Director General nabbadi@kacst.edu.sa www.kacst.edu.sa
COP-18, Side Event on
Demand Side Strategies and Buildings Energy
QNNC, Doha, Thursday November 29th, 2012

## Slide 2: Outline
Energy flow/Forecast in KSA:
  (Primary energy and electricity consumption distribution over different sectors, Energy Intensity in comparison to other countries)
Energy consumption in KSA buildings:
  Status of buildings development in KSA.
  How Electricity is consumed in the different building types in KSA.
  Examples of electricity saving is KSA buildings.
  Potential of energy saving in KSA building sector.
  Policies and regulations towards energy efficient building in KSA
Saudi Energy Efficiency Center, SEEC.

## Slide 3: Energy Flow in KSA
Year | 2008 | 2028
Primary Energy, MMBOe/day | 3.5 | 8.5
Electricity Peak Demand, GW | 37 | 108
Building sector consumed nearly 80% of the electricity generated
Notes: Need to change to toe

## Slide 4: KAS Energy Intensity
Ref. ADEME, Sept 2010.
Chart: 
| USA | Brazil | France | Germany | Turkey | UK | Russia | China | S. Korea | Egypt | Middle East | World | Saudi Arabia
2000 | 12.7311 | 1.8242 | 6.8641 | 6.1024 | 1.464 | 5.6484 | 4.8768 | 0.93214 | 5.0365 | 0.93239 | 2.2249 | 2.1655 | 5.1375
2005 | 12.8857 | 1.9512 | 7.323 | 6.5919 | 1.7752 | 5.8038 | 5.4404 | 1.6914 | 7.333 | 1.2327 | 2.6962 | 2.4313 | 6.2168
2009 | 12.1294 | 2.1031 | 7.1666 | 6.1885 | 2.0206 | 5.2331 | 5.7695 | 2.4578 | 8.4206 | 1.4681 | 3.2215 | 2.5548 | 7.347
EI showing an increasing trend
EI ~ twice the world average
kWh/capita ~ three times the world average

## Slide 5: Status of buildings development in KSA
Chart: Building Stock in KSA
| Category 1
Non-resedential Building | 6.3
Resedential Buildings | 5.1
Percentage of Residential Buildings by Region | 
Central | 30 %
Western | 35 %
Eastern | 15 %
Other regions | 20%
Nearly 70 % of all Saudi Homes are not insulated
Ref. Saudi Aramco Study, 2011.

## Slide 6: 2010 AC Installations in KSA
Chart: 
| Others | Central Region | Eastern Region | Western Region
 | 0.25 | 0.35 | 0.15 | 0.25
Chart: 
| Split | Window | Packaged | Chiller
 | 0.41 | 0.56 | 0.02 | 0.01
Total 1,478,468 units installed in 2010.
15 types of AC (e.g. window, splits, packaged)
51 manufacturers from 12 countries, 96 brands, 3,519 models.
9 local manufacturers.
Ref. Saudi Aramco Study, 2011.

## Slide 7: Typical House in Saudi Arabia: Energy Efficiency Measures
Chart: 
| House Orientation | Efficient Lighting | Reduce Air Infl. | Double Glazing | Shade Windows | Roof Insulation | Wall insulation | Improve A/C | Base Case
 | 0.4 | 0.45 | 0.48 | 0.5 | 0.55 | 0.6 | 0.65 | 0.7 | 1
When all the measures are applied (Best-In-Class) the energy use drops by 60%
Ref. Net Zero Energy Building, A. Alkhowaiter, Saudi Aramco Chair, KSU, April 3rd 2012.

## Slide 8
 | Energy Saving Measure | Annual Saving (KWH) | Annual Saving (SAR) | Cost of Measure(SAR) | Payback Period
1 | Chillers operation rescheduling | 383225 | 99639 | 0 | Immediate
2 | Stop fresh air/ventilation during the afternoon. | 359978 | 93594 | 0 | Immediate
3 | Replacement of 40W fluorescent tubes with 36W and use electronic ballast | 63554 | 16524 | 9533 | 0.57
4 | Replacement of halogen lamps with Sodium lamps | 64386 | 16740 | 20600 | 1.23
 | Total | 781142 | 226500 | 30133 | 
Sample Energy Auditing for Commercial Sector

## Slide 9
 | Energy Saving Measure | Annual saving (SAR) | Cost (SAR) | Payback period
1 | Replacement of magnetic ballast with electronic | 314,308 | 479,250 | 1.52
2 | Use of natural lighting from the roof of the workshop | 129,600 | 450,000 | 3.4
3 | Improve boiler combustion efficiency (adjusting air/fuel ratio) | 14,476 | 10,000 | 0.7
4 | Maintain pipes’ insulation and insulate exposed valves | 4,164 | 800 | 0.2
 | Total | 462,600 | 940,050 | 2.0
Sample Energy Auditing for Industrial Sector

## Slide 10: Sample Energy Auditing for Educational Building
Riyadh Technical College, old campus buildings, 2002-2003.
Average annual electricity consumption = 7070 MWh
HVAC investment based on incremental cost of efficient system
High water cooled investment due to water cost.

## Slide 11: Sample Energy Auditing for Governmental Building
Chart: 
| HVAC | Office Appliences | Lighting | Others
Electricity Consumption Distribution | 67 | 17 | 14 | 2
5 floors office building
11360 m2
2004-2007, average annual electricity consumption =1,652 MWh.
Potential savings:
  HVAC: 17 %
  (new efficient system)
  Lighting: 8 %
  (efficient fluorescent tubes and electronic ballast)

## Slide 12: Sample Energy Auditing for School Building
Chart: Summer Electricity Consumption Distribution
| AC (windows) | Lighting | Office Appliences | others
Electricity Consumption Distribution | 81 | 10 | 3 | 6
Complex of primary (200 Students) and intermediate schools (300 students).
2004-2006, average annual elec. Consum. =160 MWh.
Potential savings:
  HVAC: 40 %
  (raise EER, 5.5 to 8.5)
  Lighting: 8 %
  (EF tubes and E ballast)

## Slide 13: Examples of EE Potential in KSA: EE & LM Study
Annual Benefits | 2016 | 2021
Energy (GWh) | 10,200 (3.5%) | 29,200 (7.6%)
Peak (MW) | 5,100 (8.5%) | 10,500 (14.0%)
CO2 (000 tons) | 3,000 | 8,600
Chart: GW
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
 | 46.461 | 49.572 | 51.968 | 54.395 | 56.847 | 58.694 | 61.931 | 64.671 | 67.7247 | 71.21 | 74.824
 | 46.461 | 49.2284 | 50.7629 | 52.1204 | 53.2722 | 53.7073 | 55.9002 | 57.5705 | 59.5274 | 61.8869 | 64.3445
 | 30.5 | 32.5 | 35.2 | 38.1 | 41 | 43.7305 | 46.461
Ref. DSM Plan for KSA, ECRA, April 2011.

## Slide 14: KSA Energy Supply Chain
Wells
Upstream
Downstream
Transportation
Utilities
End User
Industrial
Terminals & Distribution
1 MWh
3.6
1.1
3.6
4.0
4.2 MWh
Ref. Net Zero Energy Building, A. Alkhowaiter, Saudi Aramco Chair, KSU, April 3rd 2012.

## Slide 15: Saudi Building Code and S&L
Published in 2009
Mandatory for public buildings and Voluntary for others
Thermal Insulation enforced for all new building by 2010
www.sbc.gove.sa
Three household appliances
Enforced since April 2010
Working on ramping up EER and developing mechanism for product control

## Slide 16: Saudi Energy Efficiency Center; SEEC
Established by the council of ministers decision # 363 dated (24/11/1431; 31 October 2010) that mandated the transfer of NEEP to a Permanent National Center for Energy Efficiency named: Saudi Energy Efficiency Center.
Temporary within KACST’s and report directory to KACST’s president.

## Slide 17: Saudi Energy Efficiency Center; SEEC
Supervised by a committee composed of representatives from related stakeholders:
Ministries of:
  Petroleum and Minerals
  Water and Electricity
  Municipality and rural Affairs
  Commerce and Industry
  Transportation
  Culture and Information
  Housing
  Finance (Customs)
Presidency of Meteorology and Environment
King Abdullah City for Atomic and Renewable Energy
Saudi Standards, Metrology and Quality Organization
Electricity & Co-Generation Regularity Authority
Royal Commission for Jubail and Yanbu
Saline Water Conversion Corporation
Clean Development Mechanism Committee
Saudi Aramco
Saudi Electricity Company
SABIC
Two Private Sector Representatives

## Slide 18
SEEC’s Mission
  Support preserving the national energy resources to enhance the national development and economy through the rationalization of energy consumption and improving energy efficiency in order to achieve the lowest possible levels of energy intensity.

## Slide 19
SEEC’s Mission…continue
  SEEC’s main activities include:
  Development of policies, rules and regulations governing EE and support their implementation.
  Support the integration of the stakeholders’ efforts to improve EE and coordination amongst them.
  Promote EE awareness at both public and institutional levels.
  Participate, as needed, in the implementation of EE pilot projects.

## Slide 20
Resources/
Infrastructure
Added Values/
\Direct Outputs
Internal Operations
National
Perspective
Vision
Mission
Values
National culture supportive of EE
Optimal Use of Energy Resources to Support The National Development
Information, consultancy and specialized services
Policies, Regulations and Specifications
Comprehensive National EE Program
Raise Public Energy Saving
Awareness
Support The Institutional EE Awareness
Leadership Role
in Raising EE Awareness,
Edu. and Training
Active Role In The Implementation
of Pilot Projects
Application of Best Practices in Project Implementation
Identify Pilot Projects Require SEEC Participation
Outstanding ability in the
development of policies,
regulations and specifications
and follow-up the application
Support Research and Studies
Build Specialized Expertise in Policies, Regulations and Specifications Development
Effective Coordination
and Integration
Among Stakeholders
Build EE database for those involved and facilitate the access to it
Develop a Practical Program for Communication and Coordination between the Concerned Parties
Human Resources
Dev. of knowledge and information sys.
Institutional structure
Dev. of Human Resources Manag. Sys.
Dev. of knowledge. Manag. Sys.
Dev. of Information System
Activation of interl. Cooperation
Work Processes Dev.
Building institutional culture
Support Moral and Financial Incentives
SEEC Strategic Map

## Slide 21
Resources/
Infrastructure
Added Values/
\Direct Outputs
Internal Operations
National
Perspective
Vision
Mission
Values
National culture supportive of EE
Optimal Use of Energy Resources to Support The National Development
Information, consultancy and specialized services
Policies, Regulations and Specifications
Comprehensive National EE Program
Raise Public Energy Saving
Awareness
Support The Institutional EE Awareness
Leadership Role
in Raising EE Awareness,
Edu. and Training
Active Role In The Implementation
of Pilot Projects
Application of Best Practices in Project Implementation
Identify Pilot Projects Require SEEC Participation
Outstanding ability in the
development of policies,
regulations and specifications
and follow-up the application
Support Research and Studies
Build Specialized Expertise in Policies, Regulations and Specifications Development
Effective Coordination
and Integration
Among Stakeholders
Build EE database for those involved and facilitate the access to it
Develop a Practical Program for Communication and Coordination between the Concerned Parties
Human Resources
Dev. of knowledge and information sys.
Institutional structure
Dev. of Human Resources Manag. Sys.
Dev. of knowledge. Manag. Sys.
Dev. of Information System
Activation of interl. Cooperation
Work Processes Dev.
Building institutional culture
Support Moral and Financial Incentives
SEEC Strategic Map

## Slide 22
Samples of SEEC’s Activities
  Developing
  a “Holistic National Energy Efficiency Program”:
    Targeting main consuming sectors (Buildings, Industry and Transportation)
    Set EE Goals for each sector
    Coordinated by SEEC
    Implemented by Stakeholders

## Slide 23: Energy Efficiency Program (EEP) objectives
Improve Kingdom’s energy efficiency in buildings, transportation, and industry
Design the energy efficiency initiatives with their energy savings goals, implementation mechanisms, and enablers
Engage key stakeholders: Government, businesses, and public

## Slide 24: EEP framework
Sectors
Buildings
Transport
Industry
New buildings
Existing buildings
New plants
Existing
plants
New
fleet
Existing
fleet
Initiatives
Initiatives
Initiatives
Initiatives
Initiatives
EE
Savings
goals
Regulations (specific to initiatives)
ESCO’s (Energy Service Companies)
Funding
Governance
Awareness
6 EE sub-sectors with EE savings goals
Initiatives to achieve the EE savings goals
Enablers to implement initiatives
EE savings

## Slide 25
Buildings objectives
Increase energy efficiency in residential, commercial and governmental buildings by achieving international level of Energy Use Intensity (kWh.year / m2)
Buildings initiatives
Products initiatives
Lead by example: government buildings
Enforce building code on new residential / commercial buildings
Retrofit existing buildings
Improve & enforce standards of A/C energy efficiency ratios EER
Mandate thermal insulation
Phase-out incandescent bulbs
Enhance other white goods energy efficiency standards
Phase I
Phase II
Phase III

## Slide 26
Resources/
Infrastructure
Added Values/
\Direct Outputs
Internal Operations
National
Perspective
Vision
Mission
Values
National culture supportive of EE
Optimal Use of Energy Resources to Support The National Development
Information, consultancy and specialized services
Policies, Regulations and Specifications
Comprehensive National EE Program
Raise Public Energy Saving
Awareness
Support The Institutional EE Awareness
Leadership Role
in Raising EE Awareness,
Edu. and Training
Active Role In The Implementation
of Pilot Projects
Application of Best Practices in Project Implementation
Identify Pilot Projects Require SEEC Participation
Outstanding ability in the
development of policies,
regulations and specifications
and follow-up the application
Support Research and Studies
Build Specialized Expertise in Policies, Regulations and Specifications Development
Effective Coordination
and Integration
Among Stakeholders
Build EE database for those involved and facilitate the access to it
Develop a Practical Program for Communication and Coordination between the Concerned Parties
Human Resources
Dev. of knowledge and information sys.
Institutional structure
Dev. of Human Resources Manag. Sys.
Dev. of knowledge. Manag. Sys.
Dev. of Information System
Activation of interl. Cooperation
Work Processes Dev.
Building institutional culture
Support Moral and Financial Incentives
SEEC Strategic Map

## Slide 27
Resources/
Infrastructure
Added Values/
\Direct Outputs
Internal Operations
National
Perspective
Vision
Mission
Values
National culture supportive of EE
Optimal Use of Energy Resources to Support The National Development
Information, consultancy and specialized services
Policies, Regulations and Specifications
Comprehensive National EE Program
Raise Public Energy Saving
Awareness
Support The Institutional EE Awareness
Leadership Role
in Raising EE Awareness,
Edu. and Training
Active Role In The Implementation
of Pilot Projects
Application of Best Practices in Project Implementation
Identify Pilot Projects Require SEEC Participation
Outstanding ability in the
development of policies,
regulations and specifications
and follow-up the application
Support Research and Studies
Build Specialized Expertise in Policies, Regulations and Specifications Development
Effective Coordination
and Integration
Among Stakeholders
Build EE database for those involved and facilitate the access to it
Develop a Practical Program for Communication and Coordination between the Concerned Parties
Human Resources
Dev. of knowledge and information sys.
Institutional structure
Dev. of Human Resources Manag. Sys.
Dev. of knowledge. Manag. Sys.
Dev. of Information System
Activation of interl. Cooperation
Work Processes Dev.
Building institutional culture
Support Moral and Financial Incentives
SEEC Strategic Map

## Slide 28: Samples of SEEC’s Activities: Energy Efficiency Awareness
Elementary School Campaign

## Slide 29: Energy Efficiency Awareness
Shopping Mall Exhibition

## Slide 30
THANK YOU